## Slide 1: Number Systems
Nazmun Nessa Moon
Assistant Professor
Department of CSE
Daffodil International University

## Slide 2: Learning Objectives
In this lecture you will learn about:
Non-positional number system
Positional number system
Decimal number system
Binary number system
Octal number system
Hexadecimal number system
Convert a number’s base
  Another base to decimal base
  Decimal base to another base
  Some base to another base
Shortcut methods for converting
  Binary to octal number
  Octal to binary number
  Binary to hexadecimal number
  Hexadecimal to binary number
Fractional numbers in binary number system

## Slide 3: Number Systems
Two types of number systems are:
Non-positional number systems
Positional number systems

## Slide 4: Non-positional Number Systems
Characteristics
  Use symbols such as I for 1, II for 2, III for 3, IIII for 4, IIIII for 5, etc.
  Each symbol represents the same value regardless of its position in the number
  The symbols are simply added to find out the value of a particular number
Difficulty
  It is difficult to perform arithmetic with such a number system

## Slide 5: Positional Number Systems
Characteristics
  Use only a few symbols called digits
  These symbols represent different values depending on the position they occupy in the number
The value of each digit is determined by
  The digit itself
  The position of the digit in the number
  The base of the number system (base = total number of digits in the number system)
The maximum value of a single digit is always equal to one less than the value of the base

## Slide 6: Decimal Number System
Characteristics
  A positional number system
  Has 10 symbols or digits (0, 1, 2, 3, 4, 5, 6, 7, 8, 9). Hence, its base = 10
  The maximum value of a single digit is 9 (one less than the value of the base)
  Each position of a digit represents a specific power of the base (10)
  We use this number system in our day-to-day life
Example
  258610 = (2 x 103) + (5 x 102) + (8 x 101) + (6 x 100)
  = 2000 + 500 + 80 + 6

## Slide 7: Binary Number System
Characteristics
  A positional number system
  Has only 2 symbols or digits (0 and 1). Hence its base = 2
  The maximum value of a single digit is 1 (one less than the value of the base)
  Each position of a digit represents a specific power of the base (2)
  This number system is used in computers
Example
101012 = (1 x 24) + (0 x 23) + (1 x 22) + (0 x 21) x (1 x 20)
= 16 + 0 + 4 + 0 + 1
= 2110

## Slide 8: Bit
Bit stands for binary digit
A bit in computer terminology means either a 0 or a 1
A binary number consisting of n bits is called an n-bit number

## Slide 9: Representing Numbers in Different Number Systems
In order to be specific about which number system we are referring to, it is a common practice to indicate the base as a subscript.
Thus, we write: 101012 = 2110

## Slide 10: Octal Number System
Characteristics
  A positional number system
  Has total 8 symbols or digits (0, 1, 2, 3, 4, 5, 6, 7).
  Hence, its base = 8
  The maximum value of a single digit is 7 (one less than the value of the base)
  Each position of a digit represents a specific power of the base (8)
  Since there are only 8 digits, 3 bits (23 = 8) are sufficient to represent any octal number in binary
Example
  20578 = (2 x 83) + (0 x 82) + (5 x 81) + (7 x 80)
  = 1024 + 0 + 40 + 7
  = 107110

## Slide 11: Hexadecimal Number System
Characteristics
  A positional number system
  Has total 16 symbols or digits (0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F). Hence its base = 16
  The symbols A, B, C, D, E and F represent the decimal values 10, 11, 12, 13, 14 and 15 respectively
  The maximum value of a single digit is 15 (one less than the value of the base)
  Each position of a digit represents a specific power of the base (16)
  Since there are only 16 digits, 4 bits (24 = 16) are sufficient to represent any hexadecimal number in binary
Example
1AF16 = (1 x 162) + (A x 161) + (F x 160)
= 1 x 256 + 10 x 16 + 15 x 1
= 256 + 160 + 15
= 43110

## Slide 12: Converting a Number of Another Base to a Decimal Number
Method
  Step 1: Determine the column (positional) value of each digit
  Step 2: Multiply the obtained column values by the digits in the corresponding columns
  Step 3: Calculate the sum of these products

## Slide 13: Converting a Number of Another Base to a Decimal Number
Example

## Slide 14: Converting a Decimal Number to a Number of Another Base
Division-Remainder Method
  Step 1: Divide the decimal number to be converted by the value of the new base
  Step 2: Record the remainder from Step 1 as the rightmost digit (least significant digit) of the new base number
  Step 3: Divide the quotient of the previous divide by the new base
  Step 4: Record the remainder from Step 3 as the next digit (to the left) of the new base number
  Repeat Steps 3 and 4, recording remainders from right to left, until the quotient becomes zero in Step 3
Note that the last remainder thus obtained will be the most significant digit (MSD) of the new base number

## Slide 15: Converting a Decimal Number to a Number of Another Base
Example:

## Slide 16: Converting a Number of Some Base to a Number of Another Base
Method
  Step 1: Convert the original number to a decimal number (base 10)
  Step 2: Convert the decimal number so obtained to the new base number

## Slide 17: Converting a Number of Some Base to a Number of Another Base
Example:

## Slide 18: Converting a Number of Some Base to a Number of Another Base

## Slide 19: Shortcut Method for Converting a Binary Number to its Equivalent Octal Number
Method
  Step 1: Divide the digits into groups of three starting from the right
  Step 2: Convert each group of three binary digits to one octal digit using the method of binary to decimal conversion

## Slide 20: Shortcut Method for Converting a Binary Number to its Equivalent Octal Number
Example:

## Slide 21: Shortcut Method for Converting an Octal Number to Its Equivalent Binary Number
Method
  Step 1: Convert each octal digit to a 3 digit binary number (the octal digits may be treated as decimal for this conversion)
  Step 2: Combine all the resulting binary groups (of 3 digits each) into a single binary number

## Slide 22: Shortcut Method for Converting an Octal Number to Its Equivalent Binary Number
Example:

## Slide 23: Shortcut Method for Converting a Binary Number to its Equivalent Hexadecimal Number
Method
  Step 1: Divide the binary digits into groups of four starting from the right
  Step 2: Combine each group of four binary digits to one hexadecimal digit

## Slide 24: Shortcut Method for Converting a Binary Number to its Equivalent Hexadecimal Number
Example:

## Slide 25: Shortcut Method for Converting an Octal Number to Its Equivalent Binary Number
Method
  Step 1: Convert each octal digit to a 3 digit binary number (the octal digits may be treated as decimal for this conversion)
  Step 2: Combine all the resulting binary groups (of 3 digits each) into a single binary number

## Slide 26: Shortcut Method for Converting an Octal Number to Its Equivalent Binary Number
Example:

## Slide 27: Shortcut Method for Converting a Binary Number to its Equivalent Hexadecimal Number
Example:

## Slide 28: Shortcut Method for Converting a Hexadecimal Number to its Equivalent Binary Number
Method
  Step 1: Convert the decimal equivalent of each hexadecimal digit to a 4 digit binary number
  Step 2: Combine all the resulting binary groups (of 4 digits each) in a single binary number

## Slide 29: Shortcut Method for Converting a Hexadecimal Number to its Equivalent Binary Number
Example: 2AB16 = ?2
Step 1: Convert each hexadecimal digit to a 4 digit binary number
216 = 210 = 00102
A16 = 1010 = 10102
B16 = 1110 = 10112
Step 2: Combine the binary groups
2AB16 = 0010 1010 1011
2 A B
Hence, 2AB16 = 0010101010112

## Slide 30: Fractional Numbers
Fractional numbers are formed same way as decimal number system

## Slide 31: Formation of Fractional Numbers in Binary Number System
Example:

## Slide 32: Formation of Fractional Numbers in Octal Number System
Example:

## Slide 33: Key Words/Phrases
Base Least Significant Digit (LSD)
Binary number system Memory dump
Binary point Most Significant Digit (MSD)
Bit Non-positional number
Decimal number system system
Division-Remainder technique Number system
Fractional numbers Octal number system
Hexadecimal number system Positional number system